## Slide 1: Introduction to IoT and It’s Application in Real Life
Sinku Kumar
Co. SST Technologies

## Slide 2: Getting Started
Download and Install Arduino IDE Software
Install the ESP8266 board support package in Arduino IDE
Introduction to ESP8266 and GPIO pins
Issues and Troubleshooting
  CP210x Driver Download and Install
Note: Don’t Install Arduino 2.0 or above

## Slide 3: History of Embedded Systems
Industrial Use
Educational or Hobby
Extended Use Case

## Slide 4: Why Espressif Systems?
Cheap
Connectivity Available
Beginner Friendly
Availability
Extended Development Support
Community Support
Industry Ready
Get Started with Arduino:
https://github.com/esp8266/Arduino

## Slide 6: Digital Input and Output
General Purpose Input and Output
pinMode(pin, MODE);
  Sets a specified pin as INPUT or OUTPUT
digitalWrite(pin, VALUE);
  Use to set the pin HIGH or LOW
digitalRead(pin);
  Use the pin to read HIGH or LOW

## Slide 7: Programs and Exercises
Programs
  Blink an LED
  Read a Button State
  Trigger Output based on input state
Exercises
  Blink 2 LEDs
  Trigger output based on input state (inverse)

## Slide 8: Analog Input and Output
Analog to Digital Converter - ADC
Digital to Analog Converter - PWM
pinMode(pin, MODE);
  Sets a specified pin as INPUT
analogWrite(pin, VALUE);
  Use to set the pin 0 to 255
analogRead(pin);
  Use the pin to read 0 or 1024

## Slide 9: Programs and Exercises
Programs
  Fade an LED
  Read a sensor value
  Trigger Output based on sensor value
Exercises
  Fade LED On, Fade LED off
  Trigger LED output based on sensor value
Challenge: Fade LED based on the duration of the button state.

## Slide 10: What am I doing?
Input
  Digital Input
  Analog Input
Output
  Analog Input
  Analog Output
Communication
  UART
Power
  Suggestions
Embedded System
Input
Output
Commu-nication
Power

## Slide 11: Communication
Serial Communication
  UART
  I2C
  SPI
  CAN
  RS232
  MODBUS
Parallel Communication
  ISA,
  ATA,
  SCSI,
  PCI and IEEE-488

## Slide 12: Universal Asynchronous Receiver Transmitter
Rx – Receiving pin
Tx – Transmission pin
Gnd – Common connection
Serial.begin(BAUD)
Serial.read();
Serial.write(‘character’);
Serial.readString();
Serial.print(“message”);

## Slide 13: Programs and Exercises
Programs
  Print message on serial console
  Control LED based on serial console input
  Print sensor data to the console
Exercises
  Print status message on serial console and control the LED using sensor value.
Challenge: Use the serial reference to use all the functions and make a solution.

## Slide 14: Network Communication
Short Range
  Bluetooth, Wi-Fi
  Zigbee
Wide Range
  LoRA, SigFox,
  NB-IoT
Cellular
  2G, 3G, 4G, 5G
Power
  Satellite
Commu-nication
Short Range
Wide Range
Cellular
Non Terrestial

## Slide 15: Network Communication
Source: All About Circuits

## Slide 16: Wi-Fi Communication
#include <ESP8266WiFi.h>
WiFi.begin("network-name", "pass-to-network");
WiFi.status() != WL_CONNECTED
WiFi.localIP()
Status using Serial Communication
https://arduino-esp8266.readthedocs.io/en/latest
/esp8266wifi/readme.html

## Slide 17: Blynk IoT Platform
Create an account on Blynk IoT Platform